- T6型铝合金固溶时效炉(铝合金淬火炉）结构简介：铝合金快速固溶炉是由炉体、炉体钢支架、可拆式炉顶、炉衬、电热元件、循环风机、风道板、炉底炉门、倍速升降机构、料架、淬火槽、运料车、控制系统及配电柜/控制柜、气动系统等组成。

1、工件转移时间短，确保铝合金固溶处理性能。

2、炉门设有自琐机构，确保可靠密封。

3、采用大流量高风压高温耐热风机，产生足够的循环风量及风压。

4、先进的热风导流系统，保证稳定可靠的炉温均匀性。

5、成熟的温度控制系统，能有效抑制温度惯性。

6、先进的料框升降机构。

二、用途：铝合金淬火炉主要用于铝轮毂、铝铸件及各种铝合金标准件的快速固溶处理。

三、主要技术参数生产案例：

| 型号 | 额定功率（KW） | 额定温度（℃） | 额定电压（V） | 相数 | 工作区尺寸（mm) | 最大装载量（kg) | 质量（kg) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| sxzzT4-75-6 | 75 | 650 | 380 | 3 | 1000X1000X1000 | 800 | 3500 |
| sxzzT4-90-6 | 90 | 650 | 380 | 3 | 1200X1200X1000 | 1200 | 4500 |
| sxzzT4-120-6 | 120 | 650 | 380 | 3 | 1200×1200×1500 | 1500 | 5200 |
| sxzzT4-150-6 | 150 | 650 | 380 | 3 | 1500X1500X1500 | 2200 | 6500 |
| sxzzT4-210-6 | 210 | 650 | 380 | 3 | 1700×1700×1800 | 3000 | 8000 |

注：若无法满足产能要求，可针对产品再行设计成固溶、时效连续式生产线。

铝合金铸造成套及配套设备以下：

Aluminum liquid degassing equipment   铝液除气设备

Aluminum melting furnace 熔铝电炉

Graphite crucible smelting furnace 石墨坩埚熔炼炉

Aluminum alloy melting furnace 铝合金熔化炉

Shoe model casting equipment 鞋模铸造设备

Plaster mould sintering furncae 石膏模具烧结炉

Melting and holding furnace 熔化保温炉

Aluminum alloy solution treatment furnace  铝合金固溶处理炉

Aluminum alloy quenching furnace 铝合金淬火炉

Aluminum alloy ageing furnace 铝合金时效炉

Aluminum alloy temper furnace 铝合金回火炉

Sealed box-type tempering furnace 箱式回火炉

Sealed box-type quenching furnace 箱式淬火炉

Box-type resistance furnace 箱式电阻炉

Bench machine type resistance furnace 台车式电阻炉