东莞市首创五金电子有限公司可以根据客户的要求设计、加工各种真空镀膜用钼舟、钨舟（蒸发舟、蒸发源）及其他稀有金属产品。产品加工采用尽量减少内部应力的工艺，来减少加工过程中对产品的损害，以增加使用寿命。采用独特工艺清洗并真空包装,以保证产品在使用前不被污染，确保您的镀膜质量。可以取代进口的同类产品。
   钼舟、蒸发舟，作为真空镀膜设备必不可少的配件，蒸发舟的选择决定了镀膜的质量。首创生产的蒸发舟（钼舟），均采用专业订制材料，自主生产、研发及设计，具有品质稳定，反映时间快，导电性能好，密封性与通透性强，可满足客户各类需求。

主要应用于一下领域。

在触摸屏领域的应用：手机、电脑、MP4等数码产品屏幕等

在信息显示领域的应用：液晶屏、各类液晶屏、等离子屏等。

在镀膜玻璃领域的应用：望远镜片、眼镜片、装饰玻璃等。

在信息存储领域的应用：磁信息存储、磁光信息存储等。

在装饰饰品上的应用：手机壳、表壳、眼镜架、五金、小饰品等镀膜。

钼舟1.规格:按用户提供尺寸制作。 2.材质:MO-1或钼基合金。密度:10.15-10.2 g/cm3 。 3.制作方式:板材经压延。 4.适应温度:可供在1400℃-1900℃以上条件使用。

采用专业订制材料，自主生产、研发及设计，材料和尺寸可根据客户产品需求来订做！具有品质稳定、反应时间快、导电性能好、密封性与通透性强等优点，深受国内外用户好评。

hermal vacuum evaporation (resistance evaporation) is a coating method used as part of the PVD process (Physical Vapor Deposition). The material that is to form the subsequent layer is heated in a vacuum chamber until it evaporates.


The vapor formed by the material condenses on the substrate and forms the required layer. Because many coating materials react with water, nitrogen and oxygen, this process is performed in a high vacuum. The high temperatures that are required are generally produced using resistance heaters or, in some cases, induction heaters, electron beams or arcs. Evaporation boats are manufactured from refractory metals such as molybdenum, tungsten or tantalum to help them withstand these high temperatures as well as the chemical aggressions caused by the coating material.